CWDS556

Closed Loop Stepping System

# Introduction

Descriptions

CWDS556 is a new generation hybrid servo driver, it combines the advantage of the servo system and stepper system，the system acts as nothing more than a high pole servo motor, the classic stepper motor noises and resonances vanish. Because the position is controlled, the motor can also no longer lose any steps up to its maximum torque.

Features

- Closed-loop control, no longer lose any steps, up to its maximum  torgue;

- higher torque and higher speed;

- Fast response;

- Reduced motor heating and more efficient;

- Zero-speed stability;

- Smooth motion and super-low motor noise;

- No Tuning and always stable;

- Lower cost.

Applications

CWDS556 is a low-cost, high-performance servo systems, suitable for a variety of large-scale automated equipments and instruments, such as low-cost, low vibration, noise, high-precision, high-speed devices, And it is ideal for applications where the equipment uses a belt-drive mechanism or otherwise has low rigidity and you don't want it to vibrate when stopping.

Electrical Specifications

| Parameter | Min | Typical | Max | Unit |
| --- | --- | --- | --- | --- |
| Input Voltage(DC) | 20 | - | 50 | VDC |
| Output Current | 0 | - | 5.6 | A |
| Pulse Signal Frequency | 0 | - | 200 | KHZ |
| Logic Signal Current | 7 | 10 | 16 | MA |

- Microstep and Dir Setting

Steps/Revolution：

| Step/Rev | SW1 | SW2 | SW3 | SW4 |
| --- | --- | --- | --- | --- |
| Default | on | on | on | on |
| 800 | off | on | on | on |
| 1600 | on | off | on | on |
| 3200 | off | off | on | on |
| 6400 | on | on | off | on |
| 12800 | off | on | off | on |
| 25600 | on | off | off | on |
| 51200 | off | off | off | on |
| 1000 | on | on | on | off |
| 2000 | off | on | on | off |
| 4000 | on | off | on | off |
| 5000 | off | off | on | off |
| 8000 | on | on | off | off |
| 10000 | off | on | off | off |
| 20000 | on | off | off | off |
| 40000 | off | off | off | off |

Motor Direction (SW5)

| Motor Direction |
| --- |
| SW5 | ON | OFF |
| Direction | Motor direction is positive | Motor direction is negative |

# 3. Connectors and Pin Assignment

The CWDS556 has four connectors, connector for control signals connections, connector for stator signal connections, connector for encoder feedback and connector for power and motor connections.

Control signal Connector

| Control Signal connector |
| --- |
| Name | Description |
| PUL+ | Pulse signal positive |
| PUL- | Pulse signal negative |
| DIR+ | Direction signal positive |
| DIR- | Direction signal negative |
| ENA+ | Enable signal positive, usually left unconnected(enable) |
| ENA- | Enable signal negative, usually left unconnected(enable) |

Figure1: Common-Cathode

Figure2: Common-Anode

| VCC | R |
| --- | --- |
| 5V | 0 |
| 12V | 680Ω |
| 24V | 1.8KΩ |

Figure 3: Typical Connection

Stator Signal Connector

| Stator Signal Connector |
| --- |
| Name | Description |
| ALM+ | Alarm Signal: OC output, Normally closed, positive |
| ALM- | Alarm Signal: OC output, Normally closed, negative |

Encoder Extension Cable Pin Out

| Name | Color |
| --- | --- |
| EGND | White |
| VCC | Red |
| EA- | Blue |
| EA+ | Black |
| EB- | Green |
| EB+ | Yellow |

Power and Motor Connector

| Name | Description |
| --- | --- |
| A+ | Motor Phase A+(Blue) |
| A- | Motor Phase A- (Yellow) |
| B+ | Motor Phase B+ (Black) |
| B- | Motor Phase B- (Red) |
| +Vdc | Power Supply Input |
| GND | Power Supply Input |

4．High voltage interface

| name | specification | Color |
| --- | --- | --- |
| U | Three phase stepper motorUphase | Black |
| V | Three phase stepper motorVphase | Yellow |
| W | Three phase stepper motorWphase | Blue |
| +Vdc | Positive pole for input power supply | +20-+50VDC |
| GND | Negative pole for input power supply | ground |

5．Typical wiring diagram

# 4. Problems and Solutions

| problems | Possible cause | solutions |
| --- | --- | --- |
| Motor is not rotating | No power supply | Check the power supply |
|  | No control signal | Check the control signal |
|  | The driver is disabled | Don’t connected the enable signal or enable the driver |
| ALM lights flashing | Supply voltage is too high or too low | Check the supply voltage |
|  | Motor line wrong connect | Check the motor wiring |
|  | Encoder line wrong connect | Check the encoder wiring |
|  | Motor line short-circuit | Check motor lines eliminate the short-circuit |
|  | Motor or drive failure | Replace the motor or drive |
|  | Lose step | Restart driver |
| Motor rotates in the wrong direction | SW5 setting wrong | Change SW5 state |
| Inaccurate Position | The Micro steps set incorrectly. | Set the correct segments |
|  | Control signal is interfered | Eliminate interference |
| Motor Stalled | Power supply voltage too low | Increasing the supply voltage |
|  | Accelerating time is too short. | Extend the acceleration time |

5. Mechanical Specifications (unit: mm)